All In One Energy Storage System

CATL Battery Solutions

|  | CATL LFP Battery，Stableandsafe |
| --- | --- |
| Safety | Module, pack, system, triple protection |
|  | Modular design，Plug and play |
| Simple | Mobile APP Monitoring |

Battery Model

Physical

| Battery type | LFP (LiFePO4) |
| --- | --- |
| System Weight | 54KG |
| Dimension (W x H x D) | 540*490*240 |
| IP Protection | IP65 |
| Warranty | 5 Year Product Warranty, |
|  | 10 Year Performance Warranty |
| Electrical |  |
| Energy Capacity | 5.12kwh |
| Usable Capacity | 4.6kwh |
| Depth of Discharge (DoD) | 90% |
| Rated Voltage | 48V |
| Operating Voltage Range | 44.8-56.5V |
| Internal Resistance | <20mΩ |
| Cycle Life | 10000cycle |

|  | Adjustable power in each phase |
| --- | --- |
| Adaptable | Support diesel generator control(DI/DO) |
|  | Supporting 200% oversized PV power |
| Efficient | On&OFF Grid parallel system |
| BluE-PACK5.1 |  |  |  |
| Operation |  |  |  |
| Max. Charge/Discharge Current | 50A/80A |
| Rated DC power |  | 4096W |  |
| Max. Charge/Discharge Power | 2825W/4096W |
| Operating Temperature Range | 0 to 50℃ charging |  |
|  |  | -10 to 50℃ discharging |  |
| Humidity |  | 0~95% (No condensation) |
| BMS |  |  |  |
| Modules Connection | Max. 4 |
| Capacity |  | 100-400Ah |  |
| Power Consumption | <2W |
| Communication |  | CAN & RS485 |
| Monitoring Parameters | System voltage, current, cell voltage, cell |
|  | temperature, PCBA temperature measurement |
| Certificate |  |  |  |
| Safety(Cell) |  | Pack: IEC/EN 62619;UN38.3 |
|  |  | Cell: IEC/EN 62619;UN38.3;UL1973 |
|  |  | *Maximum 4 battery pack in parallel. |

Hybrid Inverter Model

PV String Input

BluE-S 10KT

|  | Max. Continuous PV Input Power | 20000W |  |
| --- | --- | --- | --- |
|  | Max. DC Voltage | 1100V |  |
|  | Nominal Voltage | 720V |  |
|  | MPPT Voltage Range | 140V-1000V |  |
|  | MPPT Range (Full Load) | 420V-850V |  |
|  | Start Voltage | 130V |  |
|  | MPPT Tracker / Strings | 2/2 |  |
|  | Max. Input Current Per MPPT | 15A |  |
|  | Max. Short-circuit Current Per MPPT | 20A |  |
|  | AC Output (Grid) |  |  |
|  | Nominal AC Output Power | 10000W |  |
|  | Max. AC Apparent Power | 11000VA |  |
|  | Nominal AC Voltage | 400Vac 3W+N+PE |  |
|  | AC Grid Frequency Range | 50 / 60Hz |  |
|  | Max. Output Current | 14.5A |  |
|  | Max. Input Current | 16A |  |
|  | Power Factor (cosΦ) | 0.8leading-0.8lagging * |  |
|  | Battery Input |  |  |
|  | Battery Type | LFP (LiFePO4) |  |
|  | Nominal Battery Voltage | 48V |  |
|  | Charging Voltage Range | 40-60V |  |
|  | Max. Charging Current | 200A |  |
|  | Max. Discharging Current | 200A |  |
|  | AC Output (Backup) |  |  |
|  | Max. Output Apparent Power | 10000VA |  |
|  | Rated Output Power | 9200W |  |
|  | Rated/Max. Output Current | 14.5A/16A |  |
|  | Nominal Output Voltage | 400V |  |
|  | Nominal Output Frequency | 50/60Hz（±2%） |  |
|  | Output THDv (@Linear Load) | <3%（Linear Load） |  |
|  | Protection |  |  |
|  | Anti-islanding Protection | Yes |  |
|  | Output Over Current | Yes |  |
|  | DC Reverse Polarity Protection | Yes |  |
|  | String Fault Detection | Yes |  |
|  | AC/DC Surge Protection | DC Type II;AC Type III |  |
|  | Insulation Detection | Yes |  |
|  | AC Short Circuit Protection | Yes |  |
|  | General Specifications |  |  |
|  | Dimensions W x H x D | 540*980*240mm |  |
|  | Weight | 42kg |  |
|  | Operating Temperature Range | -25℃~+60℃ (Derating ＞45℃ ) |  |
|  | Noise (dB) | <25 |  |
|  | Cooling Type | Natural Convection |  |
|  | Max. Operation Altitude | 3000m (Derating ＞ 2000m) |  |
|  | Operation Humidity | 0~95% (No Condensation) |  |
|  | IP Class | IP65 |  |
|  | Topology | Battery Isolation |  |
|  | Communication | RS485/CAN2.0/WIFI/4G |  |
|  | Display | LCD/APP |  |

* 0.95leading-0.95lagging for Germany

# Text boxes

Felberstraße 126, 1150 Wien. www.greenInfra.at Kommunikation: email: office@greenInfra.at , Tel.: +43-660 140 40 40